## Slide 1: Device Model Summary Model ID = dtmi:com:Microchip:WBZ451_Curiosity;2 File Name = wbz451_curiosity-2.json
Type | Name | Schema | Example JSON Message/Format
Telemetry | temperature | double | {“temperature”:26.8175}
Telemetry | button_event | Object | {“button_event”:{“button_name”:“USR-BTN”, “press_count”:7}}
Property (Read Only) | firmwareVersion | string | {“firmwareVersion”:“19.7.7.19759”}
Property (Read Only) | ipAddress | string | {“ipAddress”:“192.168.1.24”}
Property (Writable) | rgb_led_blue | dutyCycle | {“rgb_led_blue”:{“ac”:200,“av”:13, “ad”:“confirmed”,“value”:0}}
Property (Writable) | rgb_led_green | dutyCycle | {“rgb_led_green”:{“ac”:200,“av”:48, “ad”:“accepted”,“value”:100}}
Property (Writable) | rgb_led_red | dutyCycle | {“rgb_led_red”:{“ac”:200,“av”:29, “ad”:“acknowledged”,“value”:0}}
Property (Writable) | led_user | LedState | {“led_user”:{“ac”:200,“av”:104, “ad”:“success”,“value”:3}}
Property (Writable) | telemetryInterval | integer | {“telemetryInterval”:{“ac”:200,“av”:55, “ad”:“OK”,“value”:10}}
Property (Writable) | debugLevel | Enum | {“debugLevel”:{“ac”:200,“av”:8670192, “ad”:“noted”,“value”:5}}
Command (Request) | reboot | Object | {“delay”:“PT5S”}
Command (Response) | reboot | Object | {“status”:“success”,“delay”:5}
Command (Request) | echoMsg | Object | {“echoMsgString”:“Hello World!!!”}
Command (Response) | echoMsg | Object | {“echoMsgString”:“Hello World!!!”}